BENG401 –

Layout methods and techniques for printed circuit boards.

- Design a simple circuit.

  - What is a simple circuit?	One that contains at most one integrated circuit and passive components. Assume you will have power from batteries or a DC power supply. Assume also that you will have an oscilloscope to look at the output of your circuit.

- Before going to the layout, make sure you can get the parts for your circuit. Several companies send out samples of their ICs. Here are some suggestions:

  - www.maxim-ic.com (best place for samples)

  - www.analog.com (max of 2 ICs per order)

  - www.linear.com

  - www.ti.com

- Decide on the software you will use for layout. If you already have a schematic (e.g. in PSpice/Orcad) then it is better to just use the same software. In that case look for “autoroute” options when transferring from schematics to layout.

- Check that your software allows you to export or print your layout in “mirrored” format. This will be important when we etch the circuit.

- Open the layout software. Here I assume you have a drawing of your circuit, with terminal numbers and right connections.

- Select components with appropriate footprints.

- Connect components as in your schematics.

- Here are some tips:

  - Use as thick tracks as you can.

  - Add a lot of labels, so you don’t get lost when we etch the circuit

  - Remember that SOIC ICs don’t need to be mirrored, but DIPs do.

  - Avoid 90 degree tracks: make them at 45 degree angles.

  - Add bypass capacitors

  - Make your circuit as small as you can (in terms of area of the PCB).

- After the layout, save your file.

- Send it to Nathalia (npeixoto@gmu.edu)

- Print it at 1:1 scale, mirrored.